Adapting a fresh Debian BeagleBone Black for use in my networks.

2GB eMMC flasher image from <http://beagleboard.org/latest-images>

1. Default user/pw is debian/temppwd.
2. What is the starting disk space situation? df -h
3. Find the large installed packages and remove any that are not needed.
  1. dpkg-query -Wf '${Installed-Size}\t${Package}\t${Description}\n' | sort -n
  2. freepats, libgl1-mesa-dri, libgtk2.0-common, libflite1, gnome-icon-theme, libsane, libsane-common, libgtk-3-0, gnome-accessibility-themes, gnome-themes-standard-data,xrdp,apache2,autoremove
4. take a look at the autostart daemon list and remove as appropriate.
  1. runlevel
  2. N n
  3. ls /etc/rc{n}.d/S*
5. df -h
6. Sudo apt-get update, sudo apt-get upgrade
7. sudo dpkg-reconfigure tzdata; Pacific-new
8. sudo apt-get install mg
9. change /etc/hostname to new name
10. ifconfig -> add MAC & IP to /etc/dnsmasq.dhcp-hostsfile on corvus 9.
11. adduser logan, adduser logan sudo
12. put a copy of authorized_keys in ~/.ssh/
13. change the ssh port in /etc/ssh/sshd_config to something unique (eg, 22xxx)
14. Add MAC to wap if this host needs wifi access to a limited network.
15. Add MAC and port forwarding to secondary router if needed
16. df -h
17. Install at will!

Date	Host	Size	Used	Available	% Used
12/03/14	Shadow	1.7G	1007M	583M	64.00%